## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26168
Problem Statement Title- AI-ML based Intelligent Dead Reckoning system for seamless navigation
Theme- Smart Vehicles
PS Category- Software
Team ID-
Team Name (Registered on portal) - STARK

## Slide 2: AI-ML based Intelligent Dead Reckoning system for seamless navigation
Proposed Solution: NavIQ App
STARK
1. Sensor Ingestion & Gravity Alignment
• Continuously capture raw IMU data (Accelerometer & Gyroscope) at high polling rates (100Hz+) natively from the smartphone. • Apply Principal Component Analysis (PCA) to isolate the Earth's gravity vector (1g). • Use robust Coordinate Rotation to instantly align the phone's erratic physical orientation to a standard "road horizon" frame.
2. Edge AI & Sensor Fusion 1D-CNN Velocity Predictor (Key Innovation): • Deploy a 1D Convolutional Neural Network directly on the edge to analyze vibration patterns rather than using traditional integration math. • Filter out human movement noise and directly output highly accurate forward velocity vectors.
3. Map-Matching & Correction • Load a digitized graph of the tunnel/road network topology. • Utilize a Hidden Markov Model (HMM) equipped with the Viterbi algorithm to analyze trajectory probabilities. • Mathematically it would snap drifting (X, Y) coordinates back onto the nearest logical road segment. • Guarantee absolute lane-level accuracy despite prolonged GNSS blackouts.( top requirement of the solution ).*close to single lane accuracyy
Key Features Zero Vehicle Dependency: Treats the car as a black box; relies 100% on smartphone sensors without OBD-II. Vibration Analysis: Uses a 1D-CNN to infer speed from accelerometer noise instead of error-prone math. Seamless Transition: Instant handoff from GPS to AI Dead Reckoning via Flutter platform channels. Edge Processing: Low-latency, offline inference running natively on the device.

## Slide 3: TECHNICAL APPROACH
STARK
• Frontend: Flutter(Android/iOS) • Programming Languages: Python, Dart, C++ (FFI) • Edge Engine: ONNX Runtime, Python Data Processing • Sensors & APIs: Smartphone IMU (Accelerometer, Gyroscope), OpenStreetMap (OSM) • AI / ML: PyTorch, 1D-CNN (Velocity Prediction), Unscented Kalman Filter (UKF), Hidden Markov Model (HMM) • Training Dataset/Raw CSVs: GitHub

## Slide 4: FEASIBILITY AND VIABILITY
STARK

## Slide 5: IMPACT AND BENEFITS
STARK

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
Your Team Name

## Slide 7
Kindly keep the maximum slides limit up to six (6). ( Including the title slide)
Try to avoid paragraphs and post your idea in points /diagrams / Infographics /pictures
Keep your explanation precise and easy to understand
Idea should be unique and novel.
You can only use provided template for making the PPT without changing the idea details pointers (mentioned in previous slides).
You need to save the file in PDF and upload the same on portal. No PPT, Word Doc or any other format will be supported.
Note - You can delete this slide (Important Pointers) when you upload the details of your idea on SIH portal.
IMPORTANT INSTRUCTIONS
Please ensure below pointers are met while submitting the Idea PPT: